## Slide 1: The evolving Internet industry Disaggregation, SDN and NFV
CS144 An Introduction to Computer Networks

## Slide 2: Coming up later this week….
Wednesday: Jeff Mogul (Google)
He will build on some of the things you will learn today.
Friday: (Nick) Network Virtualization.

## Slide 3
David D. Clark
Chief Protocol Architect, Internet
1981 - 1989

## Slide 4: Architectural Principles
Dumb and simple
i
Streamlined, fast, low-cost, easy to maintain, infrequent upgrades.
Reliable in-order delivery can be built on top, at the end-points.
i
Intelligent end-points (computers).
1
2
Notes: ADD: LAYERS OF ABSTRACTION????

## Slide 5: Architectural Principles
Decentralized control
i
Rapid organic growth
3
Notes: : Four nodes
UCLA, SRI, UCSB, Utah.

## Slide 6: Tension
The Internet was carefully designed …
To be simple and streamlined.
To have decentralized control: Lots of individually controlled pieces.
Which led to …
Explosive organic growth of the Internet.
A great business for companies selling routers.
simple and streamlined
A great business
Notes: About $100B per year. 70% gross profit margin. Which means for every $100 of goods sold, they cost $30 to build. Not bad.
So there is a business paradox here. Or rather, the situation is not stable: Simple and Streamlined is at odds with “A great business” <click>
There are two ways to break the instability: Either the Internet becomes a simple and streamlined commodity and is not particularly profitable. This would have been the social good.
Or, we break the simple and streamlined to justify keeping the profit margins high, and keeping others out of the business. Which would you do if you had a very successful, great business?

## Slide 7: What public Internet routers do
Large Public Internet Router

## Slide 8
Hardware
Hardware
Hardware
Hardware
Software
Software
Software
Software

## Slide 9
function Dijkstra(Graph, source):
for each vertex v in Graph:
dist[v] := infinity ;
previous[v] := undefined;
dist[source] := 0 ;
Q := the set of all nodes in Graph ;
while Q is not empty: // The main loop
u := vertex in Q with smallest distance in dist[] ;
remove u from Q ;
if dist[u] = infinity:
break ;
for each neighbor v of u:
alt := dist[u] + dist_between(u, v) ;
if alt < dist[v]:
dist[v] := alt ;
previous[v] := u ;
decrease-key v in Q;
return dist[], previous[];
end function
Edsger Dikjstra
1930-2002
Photo: Hamilton Richards
Notes: Edsger Dikjstra – 1956 (publushed 1959)
Takes

## Slide 10
Hardware
Hardware
Hardware
Hardware
1
2
3
B
“If , send to 3”
B
Software
Software
Software
Software
Data
B
B
“If a packet is going to B, then send it to output 3”
Figure out which routers and links are present.
Run Dijkstra’s algorithm to find shortest paths.

## Slide 11
Hardware
Hardware
Hardware
Hardware
1
2
3
B
“If , send to 3”
B
Software
Software
Software
Software
Figure out which routers and links are present.
Run Dijkstra’s algorithm to find shortest paths.
95%
5%

## Slide 12
Hardware
Hardware
Hardware
Hardware
Software
Software
Software
Software
Figure out which routers and links are present.
Run Dijkstra’s algorithm to find shortest paths.
95%
5%
50,000 lines of code
50,000 lines of code
50,000 lines of code
Building a reliable distributed system is really hard!

## Slide 13: Number of published Internet RFCs
Chart: 
Notes: First one published April 7, 1969
Most of these are written and publised by the router companies themselves.
As a result, the

## Slide 14: By 2005
Internet routers were complex: Over 100M lines of source code
They were closed and proprietary, vertically integrated, expensive.
Very hard to manage or control as a network. No clean APIs.
ISPs felt under a “stranglehold” by the router manufacturers
Internet research community was frustrated:
  Internet was “ossified”
  Easy to invent new ideas; but hard to test and deploy

## Slide 15: Two parallel trends
Research community
New programs: Clean Slate Program, NSF programs
New research: Questioning closed ecosystem
New switch API: OpenFlow
New open source: Control planes, switches, emulators
Networking industry
Rise of data centers
  Rise of Linux
  Availability of merchant switch chips
  Disaggregation of servers
ISPs under stress
  Falling consumer prices
  Need to differentiate
Somehow, control needed to move from the equipment vendors to those who own and operate networks
1
2

## Slide 16: Example: Data Center Owner
Cost
500,000 servers
25,000 switches
$10k per switch = $250M
$2k commodity switch = $50M
Savings in 5 data centers = $1B
Control
More flexible control of traffic
Tailor network as needed
Quickly improve and innovate
e.g. Google B4 network from 50% to 95%

## Slide 17: Example: Internet Service Providers
Global IP traffic growing 50% per year
End-customer monthly bills stay the same
Therefore, cost of ownership needs to reduce 50% per Gb/s per year
But in practice, reduces by <20% per year
$30/month
time
Growth in traffic
Revenue
Total cost

## Slide 18: Research community in 2006
Stanford Clean Slate Program “What would we do if we started (the Internet) again?”
2. Martin Casado and the Ethane Project

## Slide 19: How difficult is it to define all network operations in software, outside the datapath?
2006
35,000 users
10,000 new flows/sec
137 network policies
2,000 switches
2,000 switch CPUs
Stanford campus

## Slide 20: Crazy question: What if software decides whether to accept each flow, and how to route it?
A
B
[Sigcomm ’07, Kyoto]
Controllers
Check flow against policy
Pick route

## Slide 21: How many $400 servers do we need for 35,000 Stanford users?
Answer: Less than one!

## Slide 22: If we can define network behavior outside the datapath, then eventually we will.

## Slide 23: Software Defined Network (SDN)
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Control
Control
Control
Control
Control
Global Network Map
Control Plane
Control
Program
Control
Program
Control
Program
OpenFlow

## Slide 24
Forwarding
Forwarding
Forwarding
Forwarding
Dijkstra
Network OS
IS-IS
BGP
MPLS
Firewall…
Global Network Map
Notes: Design distributed system once, then reuse for many control programs.
Disentangles the two. Simplifies the control programs.
In classes, now have students create new control programs to change the behavior of the network in a few days. Before it took a team of 5-10 engineers several months.

## Slide 25: Quickly led to…
OpenFlow, SDN, Open vSwitch, network virtualization, …
In 2005, every data center and ISP was built using closed, proprietary routers.
Today, the top 10 data center owners all build their own, and write their own software (or use open source)

## Slide 26: Computer Industry
Specialized
Operating System
Specialized
Hardware
Specialized
Applications
App
App
App
App
App
App
App
App
App
App
App
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
Microprocessor

## Slide 27: Networking Industry
Switch Chips
Specialized
Operating System
Specialized
Hardware
Specialized
Features
App
App
App
App
App
App
App
App
App
App
App
Open Interface
Open Interface
Control Plane 1
Control Plane 2
NOX
Beacon
ONIX
POX
ONOS
Flood light
Trema
ODL
Ryu

## Slide 28: Network Function Virtualization (NFV)
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Middlebox
Middlebox
Middlebox
Middlebox
Public Internet
Firewalls
Load-balancing
NAT
Boundary routers
Deep Packet Inspection
DDoS Mitigation

## Slide 29: Network Function Virtualization (NFV)
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Middlebox
Public Internet
VM
VM
VM
VM
VM
VM
Packet
Forwarding
Packet
Forwarding
Firewalls
Load-balancing
NAT
Boundary routers
Deep Packet Inspection
DDoS Mitigation

## Slide 30: With hindsight, Disaggregation, SDN and NFV were inevitable
Part of a bigger trend towards the owners and operators of networks taking control of how they work

## Slide 31: Inevitable because…
Rise of Linux.
Rise of baremetal servers and data centers.
SDN: Rise of merchant switching silicon.
NFV: Rise of computer virtualization.

## Slide 32: “The Future of Networking and the Past of Protocols” Scott Shenker 2011
link
Notes: The best intro to what SDN is about from a technical viewpoint…

## Slide 33: Coming up later this week….
Wednesday: Jeff Mogul (Google) He will build on some of the things you will learn today.
Friday: (Nick) Network Virtualization.